## Slide 1: Part 12: Tools, Machinery and Equipment: Roll-on/roll-off Containers
Addition of new sections to address safety in terms of design, refurbishment, maintenance, reaper and inspection of roll-on/roll-off containers to prevent serious injuries to workers.
Adoption of ANSI Z245.30-2008 as a result of incidents involving the failure of structural component of these containers causing serious injuries to workers.
12.176-184: Amendment provides new sections
related to safety requirements for roll-on/roll-off containers through the adoption of the ANSI Z245.30-2008 standard.
Notes: Part 12, Tools, Machinery and Equipment, has been amended to provide new sections related to safety requirements for roll-on/roll-off containers through the adoption of the ANSI Z245.30-2008 standard.
Currently, roll-on/roll-off containers are not specifically covered by the OHSR resulting in inadequate safety in terms of their design, refurbishment, maintenance, repair and inspections. Some aspects are covered in Part 4, General Conditions and Part 12, Tools, Machinery and Equipment, of the OHSR and the Part 4 of BC Motor Vehicles Act. Due to the number of incidents involving the failure of structural components causing serious injuries to workers, it was determined that there was a need for a new section that specifically addresses roll-on/roll-off containers.
The adoption of ANSI Z245.30-2008 resulted from incidents involving the failure of structural components of these containers causing serious injuries to workers. The investigation following an incident where the door of the roll-on/roll-off container fell off its hinges and struck the worker causing serious injury indicated that these containers were not designed or built to any uniform standards. They also tend to be poorly maintained, increasing the possibility of the risk of injury to workers. On construction sites they are subject to being overloaded and banged about when other heavy duty machinery is used to load these containers.

## Slide 2: Part 12: Tools, Machinery and Equipment
ANSI Z245.30-2008
Establishes safety requirements for all types of waste containers (varying design, size etc.)
Specifies responsibilities of all persons likely to use waste containers (manufacturers and users who will modify, operate, repair and maintain containers)
Part 12: Tools, Machinery and Equipment: Roll-on/roll-off Containers
Notes: The ANSI Z245.30-2008 will assist manufacturers, installers, modifiers, owners, employers, waste service organizations and employees.
  Note to speaker: Refer participants to Table of ANSI Z245.30-2008 sections relevant to roll-on/roll-off containers following the Part 12 amendment and briefly review.
The ANSI establishes safety requirements for all types of waste containers which may vary in size, design and other characteristics.
However, it is important to note that Section 1.2 of the ANSI clearly states that this standard does not apply to containers intended for use by householders for their individual use which are not to be handled by mechanical container lifting and dumping mechanisms.
This standard also specifies the responsibility of all persons who are likely users of the roll-on/roll-off containers which includes manufacturers, as well as users who will modify, operate, repair and maintain these containers.

## Slide 3: Part 12: Tools, Machinery and Equipment
12.175- Definitions
‘Roll-on/roll-off container ‘ is:
(a)Typically used to receive, store and transport refuse
(b)Designed to be used with a vehicle equipped with hydraulic or mechanical tilt-frame and hoist-type equipment, commonly referred to as roll-offs or hook-lifts.
Part 12: Tools, Machinery and Equipment: Roll-on/roll-off Containers
Notes: A roll-on/roll-off container is a container that is typically used to receive, store and transport refuse, and is designed to be used with a vehicle equipped with hydraulic or mechanical tilt-frame and hoist-type equipment, commonly referred to as roll-offs or hook-lifts.

## Slide 4: Part 12: Tools, Machinery and Equipment
12.176 – Safety standard
Section 1 adopts ANSI Z245.30-2008 as safety standard from the date when these regulations are promulgated, February 01, 2015
Suppliers must ensure containers are designed and manufactured in accordance with the standard.
Employers must ensure workers handle containers in accordance with the standard.
Part 12: Tools, Machinery and Equipment: Roll-on/roll-off Containers
Notes: Section 12.177(1) adopts ANSI Z256.30-2008 as the safety standard from the date when these regulations are promulgated February 01, 2015.
Subsections 1 and 2 also state the responsibility of the suppliers and employers.
Suppliers and manufacturers must ensure containers are designed and manufactured in accordance with the requirements of the safety standard
and employers must ensure workers handle containers in accordance with the standard.

## Slide 5: Part 12: Tools, Machinery and Equipment
12.177 – Protection against hazards
Owners and employers are obligated to ensure that persons are not exposed to specified hazards:
  Rupture or disintegration of lifting eye, cables, anchors, latches, doors, guards or ladder rungs.
  Unintended or premature discharge of any thing or substance produced, used or stored in the container
Part 12: Tools, Machinery and Equipment: Roll-on/roll-off Containers
Notes: Section 12. 178 addresses the obligation of an owner of a container and an employer to ensure that persons are not exposed to specified hazards due to poor maintenance.
Hazards identified in section (a) include rupture or disintegration of lifting eye, cables, anchors, latches, doors, guards or ladder rungs. And section (b) identifies being hit or struck by the unintended or premature discharge of any thing or substance produced, used or stored in the container.
The risk of being struck by a roll-on/roll-off container door is well known in the waste industry in other jurisdictions as well.
A worker in the United Kingdom had his jaw shattered by the locking mechanism of the waste container on the vehicle he was driving. The injury happened as the worker removed the locating pin form the handle holding the rear door of the container shut. Due to pressure exerted form the load, the handle sprang open striking the worker in the face.

## Slide 6: Part 12: Tools, Machinery and Equipment
Section 1
Drivers are required to conduct a visual inspection for defects that may be a hazard prior to loading
Section 2
If a defect that may be a hazard is identified:
  (a) driver must notify employer
  (b) if no employer, driver much notify owner of container
12.178 (1) and (2) – Visual inspection
Part 12: Tools, Machinery and Equipment: Roll-on/roll-off Containers
Notes: There is a gap in regulations as well as jurisdiction relating to the period before a container is loaded onto a truck or carrier. Once a container is loaded, it falls under the jurisdiction of the BC Ministry of Transportation and Infrastructure, CVSE. CVSE only regulates how the loads are secured to the vehicle or truck.
Under Part 4 of the BC Motor Vehicle Act Regulations, drivers or carriers are required to perform a pre and post-trip inspection to ensure that a commercial vehicle is in safe operational condition. Section 37.22(2) of the Motor Vehicle Act, lists the items requiring inspection by the driver or carrier.
  Note to speaker: Refer to Part 4 of the BC Motor Vehicle Act Regulations at the end of the speaker’s notes to support any questions or discussion.
Sections 1 and 2 of 12.179 of the OHSR complement Part 4 of the Motor Vehicle Act.
Section 1 requires the driver to walk around a container prior to it being loaded onto a truck or carrier to visually inspect for defects that may be a hazard and to ensure that the doors of the container will not open when the container is moved between the ground and the vehicle. When the container door opens during loading , the hinges become damaged, raising the risk of the door falling off its hinges.
Subsequently, as stated in subsection 2(a), if a driver identifies a defect that may be a hazard, the driver is require to notify either his or her employer and,
in reference to subsection 2(b) if the driver does not have an employer, the owner of the container must be notified.

## Slide 7: Part 12: Tools, Machinery and Equipment
12.179 – Removal from service
Upon notification of a defect that may be a hazard, the notified person must:
  (a) - withdraw the container from service immediately, or
  (b) - if not practicable to withdraw container from service, arrange for safe removal to a place where it can be unloaded and/or repaired.
Container removed from service may not be returned until inspected by a qualified person.
Part 12: Tools, Machinery and Equipment: Roll-on/roll-off Containers
Notes: Section 12.180 sets out the obligations of the person who is notified of the defects in section 12.179 (1).
These include 2(a) withdrawing the container from service immediately, or 2(b) if it is not practicable to withdraw the container from service, arrange for the safe removal of the container to a place where its contents can be unloaded, if necessary, and the container can be repaired.
A container that has been withdrawn from service or repaired under this section may not be returned to service until inspected by a qualified person which is laid out in the next section.

## Slide 8: Part 12: Tools, Machinery and Equipment
12.180 (1) – Inspection
Conditions for inspection by a qualified person:
  (a) - after any significant structural modification, refurbishment ,or
  (b) - after any significant repair to a structural component
  (c) - after any repair under section 12.179
Part 12: Tools, Machinery and Equipment: Roll-on/roll-off Containers
Notes: Section 12.181 sets out the conditions for when a container must be inspected by a qualified person to ensure that the container meets the container safety standard.
Subsection 1a states that it must be done after any significant structural modification, refurbishment, or, as per subsection 1b, after any signification report to a structural component and, as stated in subsection 1c, after any repair under section 12.180.

## Slide 9: Part 12: Tools, Machinery and Equipment
12.180 (2) and (3) – Inspection
Section 2
Upon inspection, qualified person determines whether the container meets the safety standards.
Section 3
Inspection must be completed:
  (a) - within 30 days of modification, refurbishment or repair
  (b) - on return of container to place of ordinary storage or location
Part 12: Tools, Machinery and Equipment: Roll-on/roll-off Containers
Notes: As laid out in section 2, the qualified person must then determine whether, following the modification, refurbishment or repair, the container meets the requirements of the container safety standards.
And section 3 identifies a timeline for the inspection. The inspection is required as per section 3(a) within 30 days of the making of the modification, refurbishment or repair and as per section 3(b) on the return of the container to the place where it is ordinarily stored or located.
NOTE TO SME REVIEWERS: DEFINTION OF QUALIFIED PERSON WILL BE ADDRESSED THE FIRST TIME IT IS NOTED IN THE TRAINING.

## Slide 10: Part 12: Tools, Machinery and Equipment
12.181 – Periodic inspections
Relating to the intervals of periodic inspections, section 12.182 harmonizes with the International Convention of Safe Containers and the Canadian Safe Containers Act.
Details for scheduling of periodic inspections:
  (1) an owner or employer, as applicable must ensure that a qualified person inspects each roll-on/roll-off container to determine if the container meets the requirements of the container safety standards.
  (2) - first inspection of container manufactured before Feb 01, 2015 or date is unknown.
  (3) - first inspection of container manufactures on or after Feb 01, 2015.
  (4) - subsequent inspection of containers.
Part 12: Tools, Machinery and Equipment: Roll-on/roll-off Containers
Notes: A SME NEEDS TO THROUGHLY CHECK THIS AGAINST THE EXPLANATORY NOTES
Section 12.182 sets out the requirements of a periodic inspection program. Under section 12.1871(1) an owner or employer, as applicable must ensure that a qualified person inspects each roll-on/roll-off container to determine if the container meets the requirements of the container safety standards.
Although 6.1(3) of ANSI Z245.30-2008 states that it is the employer’s responsibility to establish and follow a program of periodic inspection, no details on intervals for such inspections are specified.
Section 12.182, relating to the intervals for periodic inspections, harmonizes with the International Convention of Safe Containers and the Canadian Safe Containers Act. - DO WE NEED THIS STATEMENT OR DOES THAT CONFUSE THINGS?
12.182 sets out the scheduling of periodic inspections. It provides a 30 month transition period during which existing containers are expected to be inspected and either repaired so that they may meet the new container safety standard or written out of service.
Section 2 outlines the schedule for first inspection of a container manufactured before February 01, 2015 or for which the date of manufacture is unknown.
Section 3 provides the schedule for first inspection of a containers manufactured on or after February 01, 2015.
And, section 4 details the schedule for when subsequent inspection of containers must be made.

## Slide 11: Part 12: Tools, Machinery and Equipment
12.182 – Record of inspection
An owner of a roll-on/roll-off container, and an employer, must keep a record for each roll-on/roll-off container that includes all of the following:
(a) the date of each inspection made under sections 12.180 and 12.181;
(b) details of any tests conducted, including testing methods and results;
(c) details of any repairs made;
(d) the date before which the next inspection must occur under section 12.181.
Part 12: Tools, Machinery and Equipment: Roll-on/roll-off Containers
Notes: A SME NEEDS TO THROUGHLY CHECK THIS AGAINST THE EXPLANATORY NOTES
Although 6.1(3) of ANSI Z245.30-2008 states that it is the employer’s responsibility to establish and follow a program of periodic inspection, no details on intervals for such inspections are specified.
Section 12.182, relating to the intervals for periodic inspections, harmonizes with the International Convention of Safe Containers and the Canadian Safe Containers Act. It sets out the scheduling of periodic inspections. It provides a 30 month transition period during which existing containers are expected to be inspected and either repaired so that they may meet the new container safety standard or written out of service.
Section 2 outlines the schedule for first inspection of a container manufactured before February 01, 2015 or for which the date of manufacture is unknown.
Section 3 provides the schedule for first inspection of a containers manufactured on or after February 01, 2015.
And, section 4 details the schedule for when subsequent inspection of containers must be made.

## Slide 12: Part 12: Tools, Machinery and Equipment
12.182 – Records of inspection
Suppliers and employers are required to maintain records for each container:
  (a) - date of each inspection made
  (b) - details of any tests conducted
  (c) - details of any repairs made
  (d) - date before next inspection must occur
Part 12: Tools, Machinery and Equipment: Roll-on/roll-off Containers
Notes: Section 12.183 requires a supplier and an employer to keep a record for each container. The record must include the following information outlined in subsections a through d.
The date of each inspection made under section 12.181 or 12.182.
Details of any tests conducted, including the testing method and the results
Details of any repairs made
The date before which the next inspection must occur under sections 12.179

## Slide 13: Part 12: Tools, Machinery and Equipment
12.183 – Withdrawal after inspection
Obligates owner of container or employer to follow recommendation so qualified person.
If container does not meet safety standard, container must be withdrawn
  (a) - temporarily until repaired, or
  (b) – permanently, if it cannot be repaired to meet the standard
Part 12: Tools, Machinery and Equipment: Roll-on/roll-off Containers
Notes: Section 12.184 obligates the owner of the container or the employer to follow the recommendations of the qualified person. If the qualified person determines, upon examination that a container does not meet the safety standard, the owner of the container or employer must withdraw it from service temporarily until it is repaired and meets the safety standard or if it cannot be repaired to meet the standard then it must be permanently removed.